Qui di seguito riporto il pinout del connettore Fakra dell'autoradio di serie RD4 installato sulla C4 

Part A 
Pin 1: audio rear right + 
Pin 2: audio front right + 
Pin 3: audio front left + 
Pin 4: audio rear left + 
Pin 5: audio rear right - 
Pin 6: audio front right - 
Pin 7: audio front left - 
Pin 8: audio rear left - 
Pin 9: not used 
Pin 10: data CAN high 
Pin 11: +12v switched remote 
Pin 12: battery 
Pin 13: data CAN low 
Pin 14: external mute 
Pin 15: not used 
Pin 16: ground. 


Part B 
Pin 1: audio right AUX 2 
Pin 2: audio ground AUX 2 
Pin 3: not used 
Pin 4: audio right AUX 1 
Pin 5: not used 
Pin 6: not used 
Pin 7: audio left AUX 2 
Pin 8: not used 
Pin 9: not used (microphone) 
Pin 10: audio left AUX 1 
Pin 11: audio ground AUX 1 
Pin 12: not used 

Part C 
Pin 1: ground CDC (cd-changer) 
Pin 2: data CAN low CDC 
Pin 3: + battery CDC 
Pin 4: audio right CDC 
Pin 5: not used 
Pin 6: not used 
Pin 7: data CAN high 
Pin 8: audio ground CDC 
Pin 9: not used 
Pin 10: audio left CDC 
Pin 11: not used 
Pin 12: not used 

Part optical 

Pin 1: fiber optic (optional) 
Pin 2: fiber optic (optional) 
Pin 3: fiber optic (optional) 
Pin 4: fiber optic (optional) 

minifuse 15amp